## Slide 1: SMART HOMES
Adrián Moreno Martínez
03/12/2019 @ Tarragona Developers Meetup

## Slide 2: What is a Smart Home?
“A dwelling incorporating a communications network that connects the key electrical appliances and services, and allows them to be remotely controlled, monitored or accessed.”
  “Remotely in this context can mean both within the dwelling and from outside the dwelling.”
https://www.housinglin.org.uk/_assets/Resources/Housing/Housing_advice/Smart_Home_-_A_definition_September_2003.pdf

## Slide 3: A bit of history
1901–1920: the invention of home appliances
1966: Echo IV, the first smart automation system
1969: Honeywell Kitchen Computer
1971: Intel 4004, the first microprocessor
1975: X10, the first general purpose home automation network technology
1991: gerontechnology
early 2000s: smart homes began to increase popularity

## Slide 6: Challenges
Heavily fragmented platforms
Very few open and accepted industry standards
Hard to develop cross-platform solutions
Security
Privacy

## Slide 7: Classification
Devices, or things
Central hub, or gateway
UI
Protocols

## Slide 8: Devices, or Things
Products
  Lights
  Blinds
  Cameras
  Presence detectors
  Door locks
  Thermostats
  HVAC systems
  Water detectors
  Speakers
  etc...
IoT classes:
  Assumed State
  Cloud Polling
  Cloud Push
  Local Polling
  Local Push
DYI
  Arduino
  Raspberry PI
  ESP8266
  RF Socket
  etc…

## Slide 9: Central hub
Proprietary software, e.g.:
  Samsung SmartThings
  Google Home or Nest Hub
  Amazon Echo
Open source software, e.g.:
  Home Assistant
  OpenHAB
  Domoticz

## Slide 10: UI
Web apps
Mobile apps
Voice assistants, e.g.:
  Google Home
  Amazon Alexa
Automation systems, e.g.:
  IFTTT
  Node-RED

## Slide 11: Protocols
Topology | Star | Mesh | Mesh
Standard | IEEE 802.11 | Z-Wave Alliance proprietary | IEEE 802.15.4
Frequency | 2.4 - 5 GHz | 865 - 926 MHz | 2.4 GHz
Transfer rate | > 1 GB/s | 20-40 KB/s | 20-250 KB/s
Range | 10-30 m | 35-100 m | 10-30 m
Power consumption | High | Very low | Very low
Encryption | AES 128 | AES 128 | AES 128
Devices limit | Unlimited (theoretical) | 232 | 65.000 (theoretical)
Device cost | € | €€€ | €€

## Slide 12: My home setup

## Slide 13: Requirements
No vendor lock-in
Single app
Single hub
Prefer Local over Cloud
  data locality
Prefer push over pull
Prefer open source over proprietary
Prefer non-Wifi devices

## Slide 14: Hub
Spare Raspberry PI 2
Home Assistant (Hass.io)
Aeotec Z-Wave Z-Stick Gen5
https://www.home-assistant.io/hassio/
https://www.amazon.es/Aeotec-Adaptador-USB-GEN5-bater%C3%ADa/dp/B00YETCNOE/

## Slide 15: Lights
Zemismart WiFi Downlights (Tuya cloud)
TECKIN WiFi E27 bulbs (Tuya cloud)
Flashed to Tasmota firmware
  MQTT protocol (local push)
https://www.aliexpress.com/item/32872319062.html
https://www.amazon.es/gp/product/B07GTHMPK5
https://github.com/ct-Open-Source/tuya-convert
https://github.com/arendst/Tasmota

## Slide 16: Blinds
Fibaro Z-Wave Roller Shutter 3
https://www.amazon.es/Fibaro-Roller-Shutter-Controlador-tecnolog%C3%ADa/dp/B07L5S38RN/

## Slide 17: Heating
Qubino Z-Wave Flush 1D Relay
https://www.amazon.es/Qubino-ZMNHND1-Potencia-Alimentado-Oculto/dp/B01545A2DK

## Slide 18: Others
Chromecast
  TV
Google Home
  Music
  Voice commands
Set-top box
  TV
OpenWeather
  Sunrise and sunset
  Outside weather (temp., hum., wind)
  Forecast
Mikrotik router
  DHCP devices

## Slide 19: DEMO

## Slide 20: Future work
Upgrade to Raspberry PI 4
InfluxDB and Grafana for advanced monitoring and dashboards
More sensors! (temperature, doors, windows, presence, ...)
Automations

## Slide 21: Thank you!
Questions?